U2G-Protocol
Documentation “just in case”

Gie “Max” Vanommeslaeghe
2023-03-13
# Introduction
This is a very quick documentation of the various packets used in my U2G project.
# Structure Definition Format
This documentation follows the SDF laid out by lcdr. A quick summary is that the value inside of []-brackets is representative of the variable type, and the string after the “-” is the name of that variable.
Tabs indicate that this variable is conditional or a part of the above variable.
For example:
[u8] – Count
[u32] – id
[u32] – value
Notates that there is an u8 or “unsigned char” containing the number of times the following variables, id and value, are repeated.

If statements are also possible:
[u8] – is_trigger_active
if is_trigger_active:
[u8] – only read when trigger is active

Structures can also contain “macros”, which look like the following:

def Vector3:
[float] – x
[float] – y
[float] – z
This can thus later be used as:

[vector3] – position
Which will mean the three floats are there, in the same order as defined.

# Network Version
The network version is something that is defined before the Message Identifier definitions in the source code. It must match the server’s network version in order for a connection to be made.

This documentation is concerning NET_VERSION = 4.

# Message Identifiers
Message identifiers are stored as a uint32 class enum. However, they are notably written in the packets as u8’s. Meaning they only take 1 byte and have a limit of 255.
Identifiers marked in dark red are packets that are sent from the server to the client.
- 135 – ID_STREAM_SETTINGS
- 136 – ID_HANDSHAKE
- 137 – ID_HANDSHAKE_RESPONSE
- 138 – ID_IMAGE_DATA
- 139 – ID_READY_FOR_DATA
- 140 - ID_CREATE_NEW_CHANNEL

# Packet definitions
[135] (Stream Settings)
Contains the settings for the client to use for this stream. Must arrive on client before RTSP accepts connections.
[u32] – port
[RakString] – codec name
[bool] – hardware encoder toggle

[136] (Handshake initiation from client)
Gets sent upon a successful base connection to the server.
[u32] – network version

[137] (Handshake response)
[bool] – did our handshake match the server’s? == true if yes. If false, then the client will be kicked from the server afterwards.

[138] (Image Data)
Contains image data for encoding & streaming over RTSP.
[u32] – width of the image
[u32] – height of the image
[u32] – size of following data
[u8] – byte of image data, in RGBA format.

[139] (Ready for data)
Empty packet. Must arrive on the server before image data gets sent to the client from the server.

[140] (Create new channel)
Empty packet. Simply executes a command to start a new EncodingClient that will connect using the same config.ini as the original.